## Slide 1
Lecture 0. Course Introduction
Prof. Taeweon Suh
Computer Science & Engineering
Korea University
COSE321 Computer Systems Design

## Slide 2: Course Information
Instructor
  Prof. Taeweon Suh
References
  원리부터 실무까지 쉽고 명확한 Arm 프로그래밍: Cortex-A9 중심으로
  ARM Architecture & Technical Reference Manual (TRM)
  Zedboard & Zynq-7000 TRM
  (Zedboard has a Zynq-7000 device from Xilinx)
Prerequisites
  Operating Systems (not strictly required)
  Computer Architecture
  Computer Logic Design
  C-programming
Class web
  http://esca.korea.ac.kr
Office hours
  After class
  By appointment at Aegineung Cafeteria 320
Contact Information
  suhtw@korea.ac.kr
  02-3290-2397
Zedboard
Zynq-7000
(from Xilinx)

## Slide 3: Objective
Understanding of computer systems through hands-on labs
  Software (ARM assembly & C) programming with Cortex-A9 based system
    Basic ARM programming
    Programming for I/O devices (GPIO, Timer & UART)
    Interrupts & Exceptions
    Cache & TLB manipulation
    TEE (Trusted Execution Environment) with TrustZone
  Hardware (Peripherals: GPIO and ?) design and integration into Cortex-A9 based system

## Slide 4: TA (Teaching Assistant)
Teaching Assistant: 서상현 (Sanghyeon Seo)
  MS student in Embedded Computing Lab at Aegineung Cafeteria 307
  Email: tjtkdgus45@korea.ac.kr
  Tel: 010-2267-7336 (cell)
  02-3290-2685 (office)

## Slide 5: Abstraction
Abstraction helps us deal with complexity
  Hide lower-level detail

## Slide 6: Abstraction Analogies
Combustion Engine in a car
Break system in a car
Abstraction layer
Driver
Machine Details
Hardware board in a vending machine
Machine Details
Customer
Abstraction layer

## Slide 7: Abstractions in Computer
Hardware Implementation
(x86)
Instruction Set Architecture (ISA)
Assembly language
or
Machine language
Operating Systems
Programming using APIs
Provides APIs (Application Programming Interface)

## Slide 8: Abstractions in Smartphones
Hardware Implementation
(ARM)
Instruction Set Architecture (ISA)
Operating Systems
Application Programming using APIs
http://arstechnica.com/apple/2012/09/detailed-analysis-of-apple-a6-core-reveals-layout-done-by-hand/

## Slide 9: A Computer System (~ 2010)
CPU
North Bridge
South Bridge
Main Memory
FSB
(Front-Side Bus)
DMI
(Direct Media I/F)
Hard disk
USB
PCIe card
Peripheral devices
Graphics card
But, don’t forget the big picture!

## Slide 10: Evolution of Computer Systems
Keep in mind that CPU and computer systems are evolving at a fast pace
CPU
North Bridge
South Bridge
Main Memory
(DDR2)
FSB
(Front-Side Bus)
DMI
(Direct Media I/F)
Core 2 Duo – based Systems
Core i7– based Systems
CPU
IOH (Input/Output Hub)
South Bridge
Main Memory
(DDR3)
DMI
(Direct Media I/F)
Quickpath (Intel) or
Hypertransport (AMD)

## Slide 11: 3rd Gen Core i7 (Ivy Bridge)-based Systems
FDI: Flexible Display Interface
DMI: Direct Media Interface
SPI: Serial Peripheral Interface
SMBus: System Management Bus
Notes: FDI or Flexible Display Interface is an interconnect created by Intel in order to allow the communication of the HD Graphics integrated GPU found on supported CPUs with the PCH southbridge where display connectors are attached. It provides a path between an Intel processor and an Intel southbridge on a computer motherboard which carries display data from the graphics controller (North Display) of the Intel processor package to the display connectors attached at some PCH (South Display) versions.

## Slide 12: 7th Gen Core i7 (Kaby Lake)-based Systems
http://www.pcworld.com/article/3152701/computers/official-intel-7th-gen-kaby-lake-review-one-big-change-makes-up-for-smaller-ones.html
FDI: Flexible Display Interface
DMI: Direct Media Interface
SPI: Serial Peripheral Interface
SMBus: System Management Bus
Notes: FDI or Flexible Display Interface is an interconnect created by Intel in order to allow the communication of the HD Graphics integrated GPU found on supported CPUs with the PCH southbridge where display connectors are attached. It provides a path between an Intel processor and an Intel southbridge on a computer motherboard which carries display data from the graphics controller (North Display) of the Intel processor package to the display connectors attached at some PCH (South Display) versions.

## Slide 13: x86 History (as of 2008)

## Slide 14: x86 History (Cont.)
32-bit (i386)
32-bit (i586)
64-bit (x86_64)
32-bit (i686)
8-bit
16-bit
4-bit
2009
2011
1st Gen. Core i7
(Nehalem)
2nd Gen. Core i7
(Sandy Bridge)
2012
3rd Gen. Core i7
(Ivy Bridge)
2013
4th Gen. Core i7
(Haswell)

## Slide 15: x86?
What is x86?
  Generic term referring to processors from Intel, AMD and VIA
  Derived from the model numbers of the first few generations of processors:
    8086, 80286, 80386, 80486  x86
  Now it generally refers to processors from Intel, AMD, and VIA
    x86-16: 16-bit processor
    x86-32 (aka IA32): 32-bit processor * IA: Intel Architecture
    x86-64: 64-bit processor
Intel takes about 80% of the PC market and AMD takes about 20%
  Apple has also been introducing Intel-based Mac from Nov. 2006
  From 2020, Apple is replacing Intel chip with Arm-based in-house M1, M2, and M3
* aka: also known as
https://www.apple.com/macbook-pro-13/

## Slide 16: Chipset
We call North and South Bridges as Chipset
Chipset has many PCIe devices inside
North Bridge
  Memory controller
  PCI express ports to connect Graphics card
  http://www.intel.com/Assets/PDF/datasheet/316966.pdf
South Bridge
  HDD (Hard-disk) controller
  USB controller
  Various peripherals connected
    Keyboard, mouse, timer etc
  PCI express ports
  http://www.intel.com/Assets/PDF/datasheet/316972.pdf
Note that the landscape is being changed!
  For example, memory controller is integrated into CPU

## Slide 17: PCI, PCI Express Devices
PCI (Peripheral Component Interconnect)
  Computer bus connecting all the peripheral devices to the computer motherboard
PCIe (PCI Express)
  Replaced PCI in 2004
  Point-to-point connection
PCI slot
PCI express slots
PCI express slot x16
http://www.pcisig.com/specifications/pciexpress/

## Slide 18: An Old GP Computer System Example

## Slide 19: PCI Express Slots in GP Systems
PCI express slot

## Slide 20: GP Computer System in terms of PCIe
North Bridge
South Bridge

## Slide 21: iPhone Generations
http://en.wikipedia.org/wiki/History_of_the_iPhone
Original iPhone
(iPhone 2G)
June 2007
iPhone 3G
June 2008
http://apple.wikia.com/wiki/IPhone_3G
iPhone 3GS
June 2009
iPhone 4
June 2010
Oct. 2011
iPhone 4S
iPhone 5
Sep. 2012
iPhone 5c iPhone 5s
Sep. 2013
iPhone 6 iPhone 6 Plus
Sep. 2014

## Slide 22: Galaxy S Series
http://phandroid.com/2012/07/17/samsung-galaxy-s-blaze-4g-gets-quick-maintenance-upgrade/
http://www.phonearena.com/news/Is-Android-4.2.2-the-end-of-the-line-for-the-Samsung-Galaxy-S-II-and-Samsung-GALAXY-Note_id41162
Galaxy S
Android 2.3.6
Single-core Cortex A8
June 2010
Galaxy S3
Android 4.0.4 Ice Cream Sandwich
Dual-core Cortex A9
May 2012
Galaxy S2
Android 2.3 Gingerbread
Dual-core Cortex A9
May 2011
Galaxy S4
Android 4.2.2 Jelly Bean
(Quad-core Cortex A15 & Quad-core Cortex-A7) or Quad-core Krait 300 (Qualcomm Snapdragon)
April 2013
Galaxy S5
Android 4.4.2 KitKat
(Quad-core Cortex A15 & Quad-core Cortex-A7) or Quad-core Krait 400 (Qualcomm Snapdragon)
April 2014
Galaxy S6 Edge
Android 5.0 Lolipop
Quad-core Cortex A53 & Quad-core Cortex-A57
March 2015

## Slide 23: iPhone 4 (Sep. 2010) Teardown
http://news.cnet.com/8301-13924_3-20006904-64.html
http://www.ifixit.com/Teardown/iPhone-4-Teardown/3130/1
GSM (Global System for Mobile communications): 2G, 3G, 4G ..
UMTS (Universal Mobile Telecommunications Systems): one of 3G technologies being developed into 4G
http://www.pcmag.com/encyclopedia/term/62034/antennagate

## Slide 24: iPhone 4 (Sep. 2010) Teardown
A4 Processor (ARM Cortex A8) designed by Apple manufactured by Samsung
GSM and more
GSM (Global System for Mobile communications): 3G
Samsung flash memory (32GB): K9PFG08
Audio Codec (Cirrus Logic)
512MB Mobile DDR

## Slide 25: iPhone 4 (Sep. 2010) Teardown
Accelerometer detects when the user has rotated the device from portrait to landscape, then automatically changes the contents of the display accordingly
Proximity sensor detects when you lift iPhone to your ear and immediately turns off the display to save power and prevent inadvertent touches until iPhone is moved away
Ambient light sensor automatically adjusts the display’s brightness to the appropriate level for the current ambient light, enhancing the user experience and saving power at the same time

## Slide 26: iPhone 5 (Sep. 2012) Teardown
http://www.ifixit.com/Teardown/iPhone+5+Teardown/10525/2
16GB NAND Flash from Hynix
3-axis gyroscope
Wi-Fi module
A6 application processor, based off the ARMv7 ISA
1GB Elpida LP (Low Power) DDR2 integrated according to Chipworks
Touchscreen controller
Accelerometer
LTE modem

## Slide 27: iPhone 5S (Sep. 2013)
First smartphone with 64-bit ARM
https://www.ifixit.com/Teardown/iPhone+5s+Teardown/17383
A7: Apple-designed 64-bit (ARMv8-A) dual-core CPU
https://en.wikipedia.org/wiki/Apple_A7

## Slide 28: iPhone 7 (Sep. 2016) Teardown
https://www.ifixit.com/Teardown/iPhone+7+Teardown/67382
32GB NAND Flash from SK Hynix
Barometric Pressure Sensor
Wi-Fi module
A10 Fusion application processor, based off the ARMv8 ISA
2GB Samsung LPDDR4
NFC Controller
A10: Apple-designed Quad-core SoC
3.3 billion transistors with TSMC 16nm FinFET
Two 2.34GHz ARMv8-A
Two energy-efficient 64-bit cores

## Slide 29: Apple A12 Bionic (2018)
https://www.eetimes.com/putting-ai-into-the-edge-is-a-no-brainer-and-heres-why/#
https://www.ifixit.com/Teardown/iPhone+XS+and+XS+Max+Teardown/113021
  Armv8.3-A
    6 (2+4) cores based on Big.LITTLE
  7 billion transistors
  7nm technology
NPU
  5 TOPS
  7% chip area
  Roughly $5.10

## Slide 30: Die Rendering Assumption from Skyjuice - A16 Bionic vs A15 Bionic -
https://www.angstronomics.com/p/apple-a16-die-analysis
Everest: High-performance core,
Sawtooth: energy-efficient core
SLC: System Level Cache
(iPhone 14)
A16 Bionic
Sep. 2022
16B transistors
Armv8.6-A
6 cores (2 performance + 4 efficiency)
16MB L2 for Everest
4MB L2 for Sawtooth
24MB SLC
(iPhone 13)
A15 Bionic
Sep. 2021
15B transistors
Armv8
6 Arm cores (2 performance + 4 efficiency)
12MB L2 for Avalanche
4MB L2 for Blizzard
32MB SLC
https://en.wikipedia.org/wiki/Apple_A16
https://en.wikipedia.org/wiki/Apple_A15

## Slide 31: Galaxy S3 (May 2012) Teardown
http://www.ifixit.com/Teardown/Samsung-Galaxy-S-III-Teardown/
Exynos 4412: Quad-core A9 with 1GB DDR2
Intel Wireless Processor
Samsung 16GB eMMC (MultiMediCard)
+ 64MB NAND Flash
http://www.samsung.com/

## Slide 32: Exynos 4412 Block Diagram
PoP: Package-on-Package
MFC: Multi Format Codec
Notes: What is PoP Memory?
DECEMBER 19, 2009
Package-on-Package or (PoP) memory was created as a way to reduce the physical size of the memory sub-system on a single board computer. The basic idea is to stack two BGA devices one on top of the other as shown above.
PoP Memory has Several Advantages Including:
More reliable manufacture because the memory sub-system can be assembled separately from the final system.
Higher memory cycle speeds due to shorter connection lengths.
Small size
This type of memory is used in handsets and other types of portable devices and is also making it’s way into mid-level products as well.
Disadvantages Include:
BGA assemble issues, can only re-ball the part a limited number of times then it must be scrapped. So, for example, if the RAM portion fails, the FLASH could be de-soldered and re-soldered to a working RAM module, but only a limited number of times.
Test issues – BGA packages do not allow access to device pins once the device is soldered down. In the case of a PoP module, since the top module is soldered to the bottom, there is no way to access the pins. Typically JTAG boundary-Scan tools can be used to test in this configuration.

## Slide 33: Galaxy S4 (April 2013) Teardown
http://www.ifixit.com/Teardown/Samsung+Galaxy+S4+Teardown/13947/2
http://www.samsung.com/
Snapdragon 600 has Krait 300 CPU
Krait has architectural similarities to ARM Cortex-A15 -- Wikipedia

## Slide 34: Galaxy S4 (April 2013) Teardown
http://www.techinsights.com/inside-samsung-galaxy-s4/
Exynos 5 Octa (Exynos 5410): quad-core Cortex-A15 and quad-core Cortex-A7 -- Wikipedia

## Slide 35: Galaxy S8 (April 2017) Teardown
http://www.techinsights.com/inside-samsung-galaxy-s4/
Snapdragon 835 (spec?)
4GB LPDDR4 RAM
64GB Toshiba NAND Flash

## Slide 36: Experiment Environment: Zedboard (Front)
512MB DDR3
= 2 x 2Gbit
MT41J128M16HA = 2Gb DDR3 with 16bit interface
USB OTG
USB UART
USB OTG (On-The-Go) is a specification that allows USB devices (such as mobile phones) to act as a host, allowing other USB devices like a USB flash drive, mouse or keyboard to be attached to them
JTAG (Joint Test Action Group) is the common name for the IEEE 1148.1 Standard Test Access Port and Boundary-Scan Architecture
USB JTAG
HDMI Transmitter
(ADV7511, Analog Devices)
Xilinx Zynq-7000
(dual-core Cortex-A9s)

## Slide 37: Experiment Environment: Zedboard (Back)
100MHz clock for PL
33.333MHz clock for PS
The PS can generate up to 4 PLL based clocks for the PL
SPI Flash can be used to initialize the PS subsystem and to configure the PL subsystem (bitstream)
SPI: Serial Peripheral Interface named by Motorola
4-bit SPI (Quad-SPI) serial NOR flash
SD (Secure Digital) Card
Audio Codec (ADAU1761, Analog Devices)

## Slide 38: Zynq-7000
XC7Z020-1CLG484C
Processing System (PS)
Programmable Logic (PL)
Block RAMs in purple
Hardware system will be provided
Software written in Assembly (and C) is downloaded to OCM or DDR

## Slide 39: Grading Policy
Exams (70%)
  Midterm: 30%
  Final: 40%
Assignments: 30%
Extra credit: 10%
  Mini-project: simple OS (operating system) design
Fail rules
  You will be given an “F” if you miss classes more than 3 times
    2 late show-ups will be counted as 1 absence

## Slide 40
Backup

## Slide 41: iPhone 5S (Sep. 2013)
First smartphone with 64-bit ARM
https://www.ifixit.com/Teardown/iPhone+5s+Teardown/17383
A7: Apple-designed 64-bit (ARMv8-A) dual-core CPU
https://en.wikipedia.org/wiki/Apple_A7

## Slide 42: Smartphone War
http://www.sleetherz.com/2011/10/smartphone-war-in-fatal-three-way-iphone-4s-vs-droid-razr-vs-galaxy-nexus/